## Slide 1: Automatic pulmonary lobe segmentation from CT scans
Background
The human lung is divided into five distinct anatomic compartments called lobes. The current lobe segmentation methods usually have some limitations: 1. heavily rely on anatomical knowledge. 2. largely ignore individual variability. 3. sensitive to noise. 4. lead to reconstruction of artifacts.
Summary
Manual fissure digitising and lobe fitting of about 20 subjects
Implement a initial PCA-based lobe segmentation method (mainly on healthy subjects)
Complete the basic user-interface workflow and interface
Renderings of the anatomy of the lungs. This shows the human lungs subdivided into the right upper (RU), right middle (RM), right lower (RL), left upper (LU), and left lower (LL) lobe.
Yuwen Zhang, Alys Clark, Habib Baluwala, Merryn Tawhai, Auckland Bioengineering Institute, The University of Auckland, New Zealand
Deform PCA model using lung surface data from PTK
Improved user-interactive correct mode of PTK
We plan to segment pulmonary lobes using a PCA-based model. With the help of the average model, we will be able to get rid of the dependence on the segmentation of other anatomic structures such as airway trees which are usually failed to be detected for pathological lungs. In addition, this method allows us to use a successful TLC segmentation to assist with FRC segmentation.
Hessian matrix fissure detection based on PCA model
Compute the fissureness probability of each voxel based on Hessian matrix
Fissure Detection
Fissure surface fitting
Remove the non-lung region
2D connected component analysis
3D connected component eigenvector based analysis
Fissure sampling result
PCA Weight Mapping Transformation
Training lobe mesh
PCA lung average model
Get mapping weights
Input
Deformed PCA lobe model
Fitted lobe mesh of a new subject
Lobe segmentation workflow with PTK(Pulmonary Toolkit)
PTK Lung segmentation
Lung surface data point (.exdata)
Lung surface fitting
PCA Weight mapping deformation
Matrix labels as lobes + add new plugin
Hessian matrix + local fissure points searching + connected component analysis
Lobe segmentation result
Improvement of correct mode
PCA lobe average model
PCA weight mapping transformation. (a) Left fitted lobe mesh. (b) Deformed PCA fissure mesh compared with manually digitising fissure data.
Red points: manual result
Green points:
automatic result
CMISS fissure surface fitting
(a)
(b)
Lung surface data generated from PTK
Deformed PCA mesh shown in PTK
Manual-selected landmarks for fissure correction
Fissure lines after correction
Lobe segmentation result shown in PTK
Future work
Improve the lobe segmentation method, especially for detection of the right horizontal fissure
Test the lobe segmentation algorithm on more subjects, especially abnormal subjects
Deformed PCA model can provide an approximate location of the fissures