## Slide 1: Automatic principal component based lung lobe segmentation from CT scans
Yuwen Zhang1, Mahyar Osanlouy1, Alys Clark1, Eric Hoffman2, Merryn Tawhai1.
1University of Auckland, 2University of Iowa
Method
Using an average shape model, we aim to get rid of the dependence on the segmentation of other anatomic structures such as airway trees, which often fail to be detected for pathological lungs. In addition, this method allows us to use a successful end-inspiratory segmentation to assist with end-expiratory segmentation, which is particularly challenging.
The human lung is divided into five distinct anatomic compartments called lobes. Current lobe segmentation methods usually have some limitations. They 1. rely heavily on anatomical knowledge, 2. largely ignore individual variability, 3. are sensitive to noise, 4. lead to reconstruction artifacts.
Background
Summary
2. Principle component analysis (PCA) model based weight mapping transformation
Training lobe mesh
PCA lung average model
Get mapping weights
Input
Deformed PCA lobe model
Fitted lobe mesh of a new subject
PCA lobe average model
3. Multi-scale Hessian matrix fissure detection
1. Lung segmentation
Lung surface data
Thresholding : parenchyma and trachea segmentation
Region growing: airway segmentation
Connected component analysis: separate left and right lung
Training lobe mesh:
Manual fissure digitising and finite element lung surface fitting
4. User-interactive fissure correction
5. Quantitative evaluation
We implemented a PCA-based pulmonary lobe segmentation method. The algorithm has accuracy of 72.5% to 92.6% for healthy cases and an accuracy of 53.8% to 85.7% for pathological cases. Compared to currently published methods, our method has the following advantages:
This new procedure does not heavily depend on prior segmentation of anatomical structures (airways/vessels)
With the help of an user-friendly interface, user can control some parameters (e.g. fissure searching size) as inputs to improve the segmentation process. A user-interactive correction of the result is also available.
A multi-scale filter is used when detecting fissure/vessel to make sure a variety of sizes of fissure/vessel can have maximum response.
Deformed PCA model can provide an approximate location of the fissures
Hessian based fissure enhancement
Remove the vessel structures
Fissure region of interest(ROI) based on PCA projection
2D and 3D eigenvector based connected component filter
Fissure candidate points
B-spline curve fissure surface fitting
1
2
6
The plan is to use this method to segment imaging of pathological lungs, as a step towards a new quantitative analysis of lung disease.
Correction region generation: Gaussian filter and boundary distance detection
Future work
5
6
4
3
10 healthy cases and 10 IPF cases were evaluated
IPF: Idiopathic pulmonary fibrosis