## Slide 1
Idiopathic pulmonary fibrosis: a study using volumetric imaging and functional data in a computational lung model
Idiopathic pulmonary fibrosis (IPF) is an aggressive idiopathic interstitial pneumonia, and often occurs in elderly adults. In IPF, fibrosis typically develops preferentially in posterior-basal lung regions, and often co-exists with emphysema. Currently it is not clear how - or whether - the spatial distribution of tissue abnormalities in IPF (including classifications of tissue type) correlate with pulmonary function tests (PFTs) and their change over time. This work aims to develop a new quantitative tool that integrates data from volumetric imaging, PFTs, and computational models for lung function, to understand differences between IPF and normal older lungs.
Yuwen Zhang, Alys Clark, Haribalan Kumar , Merryn Tawhai, Auckland Bioengineering Institute, The University of Auckland, New Zealand
Pulmonary parenchyma classification - CALIPER (Computer-Aided Lung Information for Pathology Evaluation and Ratings) classification of abnormalities based on signature mapping techniques
Tissue classfication
Normal Ground-glass Reticular Honeycomb Emphysema
Introduction
Analysis Qantitative analysis of disease from classified data
Data- Clinical IPF CT data from Auckland City Hospital 8 patients, 4 of them contain more than one time point scan for each
Analysis 2 Statistical shape model based shape analysis
Fibrosis has a consistently higher tissue density (0.34/0.41 for reticular/ground-glass) compared to normal tissue (0.28) over time. In contrast, emphysema has lower density (0.08)
Fibrosis presents predominantly in lower lobes (72%, 58%, 65% for honeycomb, reticular, ground-glass). But emphysema appears predominantly in upper lobes (73%).
Training data collection
Principle component shape feature analysis
Statistical shape model construction
Specific subject projection
The variation in shape of the lungs in the cohort can be assessed via a statistical shape model (SSM).
The most significant variation in shape (mode 1 of the SSM) relates to the anteroposterior diameter of the lung, and the ratio of apical and basal diameters
Mode 1 of the SSM is significantly different between IPF and normal subjects and correlates with percent of fibrosis (p<0.01).
There is a significant difference of right lower lobe volume and right middle lobe volume between normal old and IPF lungs (p=0.008168, 7.54E-07 respectively).
David Milne, Margaret Wilsher, Auckland City Hospital, Auckland, New Zealand
Brian Bartholmai, Department of Radiology, Mayo Clinic, Minnesota, US
Analysis 3 Patient-specific computational modelling of lung function
Tree generation
Tree mapping
Tree disease labelling
We classified the pulmonary parenchyma representing IPF features and performed quantitative analysis of IPF lungs.
Quantitative analysis combined with PFTs were used to drive a patient-specific computational modelling of lung function.
A future work is to explore the relationship between V/Q mismatching and disease distribution
Acknowledgements – Clinical data for this study was provided by Drs ML Wilsher and DG Milne, Auckland City Hospital; CALIPER analysis was conducted by Dr B Bartholmai, The Mayo Clinic.
Summary
Tree scaling
Step1: Airway and vessel tree generation with disease labeling
Step 3: V/Q distribution (gas transfer modeling)
PFT results: FRC, TLC, DLCO, FEV1.
Step 2: Ventialtion and perfusion simulation
The percentage of ground-glass decreases gradually with increasing lung height in the cranial-caudal axis. In contrast, the percentage of emphysema increases with lung height.
Mode1 -2 SD
Mode1 1 SD
Mode1 -3 SD
Mode1 3 SD
Mode1 0 SD
Simulated firbrosis distribution
Inhale volume and pressure curve
Disease perfusion distributiond
V/Q distrubution
PaO2 distribution
MIGET plot
Physiological knowledge of IPF patients: increased airway volume and vessel volume, decreased dead space, lung compliance and diffusion capacity
Paramiterize
modeling
Parameterize
modeling